## Slide 1: A Toolkit for Small-Angle Scattering Data Analysis

## Slide 2: Before we start…

## Slide 3: The plan…
Paul Butler Overview (15 min)
Steve King Basic Features (45 min)
            1D Fitting
              P(Q)
              P(Q)S(Q)
              with polydispersity
              with resolution smearing
            Correlation Functions
            Distance Distributions
Annika Stellhorn Magnetic Analysis (10 min)
Elizabeth Kelley Using the Command Line (10 min)
Paul Butler Model Writing (35 min)

## Slide 4: Model-Fitting
, , etc…
Method:
      choose a P(q) & S(q) if required
      choose a set of starting parameters
      compute I(q)
      compare the model calculation (theory) with the experimental data
      adjust some parameters
      iterate until an acceptable solution is found (hopefully…)
SasView offers:
~90 P(q)
4 S(q)
But you can add more!
Form Factor
Structure Factor

## Slide 5: The ‘Magic Square’
(r)
scattering length density
F(q)
scattering amplitude
(r)
correlation function
I(q)
scattering intensity
Real-space
Reciprocal-space
z(r)
chord distribution
loss of phase information
G()
SESANS function
P(r)
distance distribution
After Stribeck, (2007) & others

## Slide 6: Real-Space Methods (1)
Correlation Function,  (r)
describes spatial inhomogeneity in SLD in the sample
  in essence, the probability that rods of different lengths moving through the sample have equal SLD at either end
  1D: 3D:
Rieger, (2002)
extraction of lamellar parameters
SasView computes 1(r) & 3(r) + IDF
1(r) & 3(r)
I(q)
3D:

## Slide 7: Real-Space Methods (2)
few analytical expressions for  (r)
  homogeneous sphere:
  (radius, R) where 0  (r/R )  2
  see Glatter & Kratky, (1982)
  randomly-distributed 2-phase system: Debye & Bueche, (1949)
  (single correlation length,  ) Debye, Anderson & Brumberger (1957)
  randomly-distributed 2-phase system: Debye, Anderson &
  (dual correlation lengths,  &  ) Brumberger (1957)
  Moritani et al, (1970)

## Slide 8: Real-Space Methods (3)
Svergun & Koch, (2003)
(Pair) Distance Distribution Function, P(r)
in essence, a histogram of pair-wise distances between atoms in the scatterer
solve set of basis functions by Indirect Fourier Transformation (IFT)
Glatter, (1977); Moore, (1980); Hansen & Pedersen, (1991)
SasView implements the Moore method
Other implementations:
GIFT (from Glatter); GNOM (in ATSAS Suite); BIFT (in BioXTAS RAW)
Dmax

## Slide 10: The master plan…
Overview of features and new in 6.0 (10-15 min) PAUL
  Slides general overview of layout and where to find things … ethos of project? Points of contact at facilities, contributor list, contacts at SAS2024. Put stickers on “badges”
  Maybe preview of future features to come (beyond 6.0)
  Where to find help
Overview of using basic features (45 min) STEVE
  1d fit simple (polymer Gaussian coil)
  1d with structure factor (SDS data)
  Fit with polydispersity
  Impact of resolution smearing
  Correlation function
  P(R) of protein – Apoferritin .. and maybe sphere and rod?
  BONUS if time permits
    add/multiply used in response to question
10 min coffee
Note on magnetic/pol beam stuff 10 min ANNIKA
Brief look at CLI (quick demo of Caitlyn Wolf stuff?) (10 min) LIZ
Model writing (35 min) PAUL
  Different API ( add/multiply and reparam)
  Use sphere and have equations ready on on board – also in back .. how about a handout. Could point to tutorials and send pdf handout
  Step through
    Easy editor and “hand write” all equations including bessel NO polydisperse parameters
    Use scipy functions
    Use library functions
    Make polydisperse → point out the need to move 1/V out of the equation and use form_volume. Difference between z average (volume average) and number average
    Make possible to use structure factor
    Move to C
    Add beta approximation (have_fq=true)
    What if it IS a structure factor?