## Slide 1: SasView : A Small Angle Scattering Analysis Software Package
Andrew Jackson, European Spallation Source
on behalf of the SasView Collaboration

## Slide 2: SANS Refresher

## Slide 3: Anatomy of a SAS Instrument
Source
Guides
or
Optics
Wavelength
Selection
Guides
or
Optics
A1
A2
Detector
Sample
Collimation
L1
L2

## Slide 4: What do we measure?
Measure number of neutrons scattered as function of Q and ω
Intensity of scattering as function of Q is related to the Fourier transform of the spatial arrangement of matter in the sample => Correlations in Space
Intensity of scattering as function of ω is related to the Fourier transform of the temporal arrangement of matter in the sample => Correlations in Time

## Slide 5: Small Angle Scattering
Having determined that we can use scattering length density to describe our samples, we can replace the sum in
with the integral of the SLD distribution across the whole sample and normalize by the sample volume thus:
This is the “Rayleigh-Gans Equation” and shows us that small angle scattering arises as a result of inhomogeneities in scattering length density.

## Slide 6: Form and Structure Factors
The form factor for a sphere (shown above) is given by:
In small angle scattering we confuse terminology by often splitting the scattering structure factor into a Form Factor, P(q) and a Structure Factor, S(q) when considering particulate systems :
P(q) represents the interference of neutrons scattered from different parts of the same object, while S(q) represents interference between neutrons scattered from different objects. If there is no interparticle correlation (e.g. it is a dilute solution) then S(q) = 1.
If we have an isotropic solution then
where g(r) is the particle pair correlation function and is related to the interaction potential between particles.

## Slide 7: Form and Structure Factors
The form factor for a cylinder is given by:
where J1 is the first order Bessel function and ɑ is defined as the angle between the cylinder axis and the scattering vector q.
The radius of gyration of a cylinder is given by
where R is the radius and L the length of the cylinder.

## Slide 8: SANS Resolution
The intensity measured at each nominal Q value is, in fact, a sum of intensities from nearby Q vectors.
This is a result of the beam and the detector pixels having finite sizes, and the wavelength having a spread of values.
The effect is that the scattering that one would calculate is “smeared” by a resolution function.
Difficult to “desmear” reliably, therefore smear model functions in analysis.
A1
A2
Detector
L1
L2
See Mildner & Carpenter, J. Appl. Cryst.17, 1984 for the gory details.

## Slide 9: SAS Data Analysis
Model Independent
We can use an approximation from Guinier
to obtain the radius of gyration of the scattering objects assuming particulate scatterers and S(q) = 1.
Similar approximations can be made to get the cross section of cylinders or the thickness of disks. Various other model independent approaches exist to extract information from the data without a scattering model.
Model Dependent
We calculate the form and structure factors for a given scattering system and compare that with the measured scattering data. The model is fitted to the data to obtain the parameters that describe the scattering. We can simultaneously fit multiple contrasts to be able to study complex structures.
The software we will be using for this workshop is called SasView (http://www.sasview.org) and is being jointly developed by NIST, ILL, ISIS, SNS, ANSTO and ESS.
Other software packages for this kind of analysis include the NIST Igor Macros developed at the NCNR and SasFit developed at the Paul Scherrer Institute.
Indirect Fourier Transform
Since we are missing the phase information as a result of the differential cross section being related to the square of the amplitude of the fourier transform, we cannot simply take the fourier transform of our data to get back to ρ(r). Thus we must use an indirect method.
A popular implementation of this method is found in the ATSAS suite of software from Prof. Svergun’s group. SasView also has an implementation of this method.
Ab-inito Structure Generation
An approach that is popular for bio-macromolecules in solution is to generate a structure from many sub-resolution spheres and calculate what the scattering would be. That is then compared with the data and the spheres redistributed. This is repeated until agreement is found.
The ATSAS suite is the primary example of software using this method

## Slide 10: What is SasView?

## Slide 11: SasView
User friendly, open source analytical modeling of SAS data.
Current Release (3.1.2) Includes:
Large number of 1D scattering models
2D analysis for oriented objects
Batch mode
Magnetic contrast with polarisation analysis
Lots of extra tools
www.sasview.org

## Slide 12: 1D Analysis

## Slide 13: 1D Analysis
Load Data …
Select Data Sets …
Here we have SANS & USANS from latex spheres
Send to Fitting …

## Slide 14: 1D Analysis
Send to fitting …
Select a model …

## Slide 15: 1D Analysis
Send to fitting …
Select a model …
Set parameters …

## Slide 16: 1D Analysis
Send to fitting …
Select a model …
Set parameters …
Use resolution …

## Slide 17: 1D Analysis
Send to fitting …
Select a model …
Set parameters …
Use resolution …
How does it look?

## Slide 18: 1D Analysis
Choose which parameters to fit …

## Slide 19: 1D Analysis
Choose which parameters to fit …
… and press the Fit button!

## Slide 20: Constraints / Simultaneous Fit
But wait! We have two data sets of the same sample : SANS + USANS …

## Slide 21: Constraints / Simultaneous Fit
But wait! We have two data sets of the same sample : SANS + USANS …
Set up a simultaneous fit …

## Slide 22: Constraints / Simultaneous Fit
But wait! We have two data sets of the same sample : SANS + USANS …
Set up a simultaneous fit …
… with constraints

## Slide 23: Constraints / Simultaneous Fit
But wait! We have two data sets of the same sample : SANS + USANS …
Set up a simultaneous fit …
… with constraints
Now press the Fit button!

## Slide 24: Constraints / Simultaneous Fit

## Slide 25: 2D Modelling

## Slide 26: Other Features
Batch fitting …

## Slide 27: Other Features
P(r) Inversion …
SLD Calculator …
Sum & Multiplication of Models …

## Slide 28: SasView Development

## Slide 29: A little history …
Heritage: NIST IGOR macros
DANSE project output
~ 8.5% of funds were for SANS
Kickoff meeting August 2006
Where did SasView come from?

## Slide 30: Continuity …
NIST Supported initial transition from NSF funding

## Slide 31: Expansion …
Now 7 active facilities
ORNL, ISIS, NIST, ESS, ILL, TUD/RID, ANSTO
NIST Supported initial transition from NSF funding
SINE2020 Funding at ESS
First major investment since DANSE
http://sine2020.eu

## Slide 32: Development Model
Code is open source and publicly hosted at Github
1st at NIST April 2013
2nd at ISIS April 2014
3rd at ESS Feb 2015
4th in Delft hosted by TU Delft / RID March 2016
Open, Collaborative, Community Development
Bi-weekly developer calls
Code Camps
5 Year Roadmap
  http://github.com/SasView
  http://www.sasview.org

## Slide 33: The Future … is Now!
SESANS
Automatic transform of SANS model to P(z)
Example scripts for fitting SESANS data
Simultaneous fitting of SANS & SESANS
Integration of SESANS fitting into GUI
Models
New models
New model package (sasmodels)
  separation of models from GUI
  simpler addition of models by users
  speed! GPU and parallel processing
Documentation
Enhanced, updated documentation for models

## Slide 34: Current Development Team
Jurrian Bakker (TUD)
Wim Bouwman (TUD)
Miguel Gonzales (ILL)
Richard Heenan (ISIS)
Paul Kienzle (NIST)
Jeff Kryzwon (NIST)
Ricardo Leal (ORNL)
David Manicke (ANSTO)
Torben Nielsen (ESS)
Steve Parnell (TUD)
Wojciech Potrzebowski (ESS)
Piotr Rozyczko (ESS)
Adam Washington (Sheffield)
Questions?
Paul Butler (NIST)
Mathieu Doucet (ORNL)
Steve King (ISIS)
Andrew Jackson (ESS)
and thanks to the many previous contributors, particularly Jae Hie Cho and Alina Gervaise

## Slide 36: Small Angle Scattering
For a general two phase system, the Rayleigh-Gans equation leads to the result that :
and we see that as a result of the macroscopic cross section being a function of the square of the amplitude of the fourier transform of the SLD distribution, we are only sensitive to the absolute difference in SLD between the phases and not the sign.
This is known as Babinet’s Principle and means that small angle scattering cannot determine if ρ1 is greater than ρ2 from a single measurement. Thus we need additional information about the system or we need to use contrast variation.
The integral term in the equation is known as the scattering structure factor S(q) and describes the distribution of matter in the sample.

## Slide 37: Contrast Variation and Matching
In the case of ‘p’ different phases in a matrix ‘0’
Scattering is now the sum of several terms with possibly many Sij components

## Slide 38: Contrast Variation and Matching

## Slide 39: Contrast Variation and Matching
Caution! The SLD of the component you are interested in may vary with the solvent SLD either through hydrogen exchange (e.g. proteins) or through penetration of the solvent into the component (e.g. block copolymer micelles)