## Slide 2: Schedule for today
Monday 9th September (am, 11-12)
Small angle scattering introduction (H Barriga)
Introduction to modelling and SasView (W Potrzebowski)
Monday 9th September (pm, 13-14.30)
SasView hands on (W Potrzebowski)
Monday 9th September (pm, 15-17)
Site visit to MAXIV
Tuesday 10th September (am, 9-12)
MAXIV presentations
  9 am FragMAX
  10 am CoSAXS, Ann Terry
  11 am SAXS case study lecture: Lars Nilsson
Tuesday 10th September (pm, 13-17)
SANS capabilities for life science and DEMAX (W Potrzebowski, Esko Oksanen, Zoe Fisher)
Site visit to ESS

## Slide 3: About the teacher(s)

## Slide 4: Small Angle Scattering Analysis Toolkit
Integrated Structural Biology Course
Wojtek Potrzebowski
SciLifeLab Lund
wojtek.potrebowski@scilifelab.se

## Slide 5: Before we start…
www.sasview.org

## Slide 6: Learning objectives
Principles of Small Angle Scattering Data Analysis
Main functionalities of SasView
Form, structure factors and polydispersity
Newly developed features
Hands-on session
  1D fitting
  Creating custom plugin models
  Simultaneous fitting
  …

## Slide 7: User Journey at Large-Scale Facility
Experiment control
Data streaming
Data reduction
Data analysis
User Office Software
Before experiment
During experiment
During and after experiment

## Slide 8: User Journey
Experiment control
Data streaming
Data reduction
Data analysis
User Office Software
Responsibility+Expertise
Facility
Users

## Slide 9: Data analysis – facts of life
Data analysis is a part of the processing workflow
Reduced data on the disks is useless
User expertise is critical for successful data analysis
Facilities should support data analysis software but shouldn’t fully drive the process
->We need open and collaborative software tools to succeed!

## Slide 10: The SasView approach
An open, collaborative, community development
Community driven project
Supported by 10 facilities, 40 contributors (~15 active at any one time)
Small leadership team: Paul Butler (NIST), Steve King (ISIS), Wojtek Potrzebowski (SciLifeLab, formerly ESS)
Biweekly calls
Regular SasView camps and hackathons
Hosted on github: https://github.com/SasView/sasview
Pictures from Code Camps: V, VI, VIII, X
www.sasview.org

## Slide 11: Typical fitting workflow
For reduced data:
Load and plot experimental data
Define a model (form and structure factor) with parameters
Fit the parameters so that model matches experimental data
Draw scientific conclusions and publish results!

## Slide 12: Scattering Intensity
I(q) = (Δ⍴)2 nM2 P(q) S(q)
Intensity = Pre-factor * Form Factor * Structure Factor

## Slide 13: Pre factor
Adapted from Kell Mortensen, e-neutrons.org
I(q) = (Δ⍴)2 nM2 P(q) S(q)

## Slide 14: Form factors
Form factor P(q) represents the interference of neutrons scattered from different parts of the same object
I(q) = (Δ⍴)2 nM2 P(q) S(q)
Adapted from Kell Mortensen, e-neutrons.org

## Slide 15: Structure factors
Structure factor S(q) represents interference between different objects.
I(q) = (Δ⍴)2 nM2 P(q) S(q)
Adapted from Kell Mortensen, e-neutrons.org

## Slide 16: Form factors determined for different shapes
Credit: Reidar Lund (DOI:10.1007/12_2012_204)

## Slide 17: Form factor for sphere

## Slide 18: Form factor based on atomic coordinates
Monoclonal antibody protein
Maria Monica Castellanos et al. Analytical and Bioanalytical Chemistry (2018) 410:2141–2159
bi, bj – atomic form factors

## Slide 19: Structure factor
For an isotropic solution:
Diluted
Concentrated
Ordered
g(r)
g(r)
g(r)
Notes: S(q) is related to the probability distribution function of inter-particles distances, i.e. the pair correlation function g(r)
g(r) = Average of the normalized density of atoms in a shell [r ; r+ dr] from the center of a particle

## Slide 20: Determination of Structure Factor
For an isotropic solution:
g(r)
g(r)
g(r)
S(q)
S(q)
S(q)
1
1
Notes: g)r) average of the normalized density of atoms

## Slide 21: Which model should I use?
Prior knowledge
Literature search
SasView documentation
Usually, more than one model fits
Model-free analysis

## Slide 22: How to represent a virus capsid?

## Slide 23: 70+ models to explain data
Data management
Common data formats supported, including NXCansas & cansas1D
Analysis Tool Choice
&
Plotting
Polydispersity (choice of distribution and distribution parameters)
Resolution smearing (pinhole and slit)
Automatically from data or provide parameters
Wide choice of built-in models (> 70)
F(Q), S(Q) & F(Q)*S(Q)
Single, batch and simultaneous 1D and 2D fitting

## Slide 24: Fitting model to data through χ2 optimization
 | Before fit
model | 
lenght | 350 Å
radius | 35 Å
 | 416.9
After fit
400 Å
40 Å
0.03

## Slide 25: 2D fitting for oriented or magnetic particles
1D and 2D cylinder model

## Slide 26: Plugin models
Dedicated editor
Syntax and performance testing
Directly available in SasView ecosystem
Community developed models can be deposited to marketplace: https://marketplace.sasview.org/

## Slide 27: Plugin models tutorial
Available at https://www.sasview.org/download/

## Slide 28: Polydispersity
Types of polydispersity:
Size - all particles have similar shape but differ in size, e.g. nanoparticles colloids
Shape – different shape and size (e.g. oligomeric mixtures)
Conformational – particles of identical molecular mass, which adopt different conformations, e.g. disordered or flexible proteins

## Slide 29: Size polydispersity
Average intensity for a population of particles that possess size distributions
The resultant intensity is then normalized by the average particle volume

## Slide 30: Shape polydispersity
Mixture of components gives combined scattering curve:
Combined curve can be fitted to experimental data Iexp(q) to infer vk
volume fractions
normalized scattering intensities

## Slide 31: Conformational polydispersity
Flexible and disordered proteins
The same principle as for shape polydispersity:
Large number of parameters = high risk of overfitting
volume fractions
normalized scattering intensities

## Slide 32: But what if we don’t know the model
Porod (Scattering) invariant can be applied to multiphase systems
Provide independent estimate of volume fractions (porosity) and surface area (reactivity)
It can be used as sanity check

## Slide 33: Pair Distance Distribution function P(R)
P(r) - probability of finding a vector of length r between scattering centers
Gives some idea about the shape of the molecule
Dmax
P(r)
r
r
r
r

## Slide 34: Other SasView functionality
Analysis
Fitting
Invariant
Pr Inversion
Correlation Function
Tools
Data Operation
SLD calculator
Density/Volume calculator
Slit Size Calculator
Kiessig Thickness Calculator
Q Resolution Estimator
Generic Scattering calculator
Orientation Viewer
Python Shell/Editor
Image Viewer
File Converter

## Slide 35: Beyond Graphical User Interface (GUI)
Useful for batch jobs and reproducibility
Scripts can be run on computer cluster
Before fit
After fit

## Slide 36: Beyond Graphical User Interface (GUI)
Python installation
For fitting, there is no need to install sasview
Pip install sasmodels sasdata bumps
It can be run on computer clusters (also with GPU)
sasview
sasdata
sasmodels
bumps

## Slide 37: SasView collaboration
Those who bring the resources (time, effort, funds) choose what to work on
but cannot break existing experiences ...

## Slide 38: Student projects and ”external” contributions
Simultaneous SAXS and SANS fitting
Improvements in:
  Plotting
  Data structure
  Documentation
  Plugin Editor
  Slicers
  Generic Scattering Calculator
Web-based API
Pore size distributions
Contributors: Iestyn Cadwallader-Jones, Nouhalia Agouzal, Dorian Lozano, Julius Karliczek (ILL), Ellis Hewis, James Crake-Merani, Ruben Lopes (ISIS), Alex Zheng (NIST), Brayden Miller (NIST), Xael Shan (NIST), Anita Zhang (Princeton), Kristian Lytje (Arhus University)

## Slide 39: Combined SAXS and SANS
Simultaneous measurements on the same sample
Running at D22 instrument at ILL
Low-flux SAXS source
Specialized sample environment
Non-trivial data analysis
SasView (6.0.0) provides a weighting mechanism in simultaneous fitting
Notes: High-energy gamma radiation gives rise to backgrounds

## Slide 40: Generic Scattering calculator improvements
Magnetic/polarized SANS
Generic Scattering Calculator supports magnetic/polarized SANS
Coordinate data in VTK formats supported
Interacting bio-molecules
Generate scattering profile from PDB file
Save as a custom/plugin model
Use for fitting with structure factors (including beta approximation)
PDB reader and engine refactored
Validation of electron-microscopy maps using solution small-angle X-ray scattering
Kristian Lytje and Jan Skov Pedersen, Volume 80| Part 7| July 2024| Pages 493-505

## Slide 41: SasView 6.0.0-beta release
Orientation viewer available
Corfunc perspective refactored
Simultaneous fitting allows for a weighting scheme
Preferences panel with display and plotting options
Improved label handling on plots
Residuals plots refactored
PDB reader refactored
Wedge slicer added
Sasdata package separated
Custom Model writing tutorial
https://github.com/SasView/sasview/releases/tag/v6.0.0-beta-2

## Slide 42: Resources for users and contributors
Website
Documentation
  in-program & online
Written Tutorials
Video Tutorials (YouTube)
Taught Courses
  scattering schools/workshops
  university courses
Bootcamps & regional workshops
e-Learning
Slack
Linkedin
(Marketplace)
help@sasview.org
users@sasview.org

## Slide 43: Different approaches to SAS data analysis
https://www.isis.stfc.ac.uk/Pages/SANSdataanalysisOverview.aspx
Not in SasView scope

## Slide 44: ATSAS
https://youtu.be/T7r583F8qDM?si=tGViSEsWX6nYB-0v

## Slide 45
Questions?

## Slide 46: Hands-on session
New to SasView? Start here
https://www.sasview.org/documentation/
2
3
4

## Slide 47: Experimenting with SasView
Download SasView 6.0.0 and try out new features:
https://github.com/SasView/sasview/releases/tag/v6.0.0-beta-2
Run SasView from the script:
Setup python environment
Install required packages
Play with some of the notebooks: https://github.com/SasView/documents/tree/master/Notebooks

## Slide 48: Thank you!

## Slide 49: Thank you, Sponsors!!

## Slide 50: Correlation function