## Slide 1: Small Angle Scattering Data Analysis with SasView
What SasView can do for you and what you can do for SasView?
PRESENTED BY WOJCIECH (WOJTEK) Potrzebowski

## Slide 2: Agenda
A few topics to cover…
SAXS
SANS
Data analysis
Notes: The one partictular challange of this presentation is to provide enough background information to the understand what SasView is good for. I’ve watched few prievious webinars from the series and I assume that audience will simillar and therefore selected this contentent. I will have to clain thoiught that I won’t be able to cover alll these topics in a great detail. The main topic of this presentation is SasView, however it cannot be discussed for general audience without introducing

## Slide 3: What is Small Angle Scattering?
Small-angle scattering uses X-ray (SAXS) or neutron (SANS) scattering at small scattering angles to investigate the structure at length scales from 1 - 100 nm.
Barré L. (2016) Contribution of Small-Angle X-Ray and Neutron Scattering (SAXS and SANS) to the Characterization of Natural Nanomaterials

## Slide 4: What can we learn from SAS experiment?
SAS provides information about:
Size of particle
Shape of particle
Inter-particle interactions
Orientation
Magnetic properties

## Slide 5: What can we study with SAXS and SANS?
Aerogel, alloys
Bio-macromolecular assemblies, bone
Colloids, complex fluids, catalysts
Detergents, dairy (casein micelles)
Earth science, emulsions
Fluid adsorption in nanopores, fuel cells, food science (chocolate)
Gelation, green solvents
SAS applications A to Z
High pressure, high temperature, hydrogen storage, helium bubble growth in fusion reactors
Implants (UHDPE)
Jelly Kinetics (e.g. of polymerization or protein folding)
keratin
Liquid crystals
Magneticflux lines, materials science
Nano-anything
Orientational order
Polymers, phase behavior, porosity
Quantum dots (GISAXS)
Rubber, ribosome
Soft matter, surfactants, switchgrass
Time-resolved, thermodynamics
Uranium separation
Vesicles, viruses
Wine science, Xylose isomerase
Yttrium-stabilized zirconia (YSZ)
Zeolites

## Slide 6: How SAXS and SANS are related?
X-rays
Readily available
Lab-based sources
Synchrotrons
Massive fluxes possible
Sub-ms time-resolved studies
Smaller sample required (> 2.5 µl)
Physics of SAXS and SANS don’t really differ, but their properties differ a great deal
Neutrons
Large user facilities only
Spallation sources
Reactors
No radiation damage
Time-resolved studies
Larger sample required (>150 µl)
Contrast variation
Magnetism
LOKI europeanspallationsource.se
Experiments using neutrons usually have higher entry barrier!
NANOPIX mini www.rigaku.com

## Slide 7: What kind of information do we get?
q[1/nm]
I(q)
1D SAS data
2D SAS data for oriented or magnetic systems

## Slide 8: What kind of information do we get?
Considerable loss of structural information!
q[1/nm]
I(q)
Defining correct model is very important and the risk of overfitting to data is high!
Potrzebowski et al. PLOS Comp. Biol, 2018

## Slide 9: Typical SAS data analysis workflow
Acquire data -> I(q)
Define a model with some free parameters
Calculate scattering pattern for that model for a given set of values for parameters
Fit the parameters so simulated data based on model matches experimental data
Credit: T. H. Rod

## Slide 10: Defining model is crucial for data analysis
n is the number density of particles
F(q) is the form factor (particle shape)
S(q) is the structure factor (particle interactions)
Cylinder radius = 40Å, lenght = 200Å
Hardsphere, effective radius = 50Å
Protein structure coordinates

## Slide 11: Fitting model to data is typically done through χ2 optimization
 | Before fit
model | 
lenght | 350 Å
radius | 35 Å
 | 416.9
After fit
400 Å
40 Å
0.03

## Slide 12: Typical SAS data analysis workflow
Acquire data -> I(q)
Define a model with some free parameters
Calculate scattering pattern for that model for a given set of values for parameters
Fit the parameters so simulated data based on model matches experimental data
Credit: T. H. Rod

## Slide 13: SasView history
SasView originates from NSF funded project DANSE (2006)
Turned into Community project in 2013
Supported by 9 facilities, 40 contributors (~15 active at any one time)
Management: P. Butler (NIST), M. Doucet (ORNL), A. Jackson (ESS), S. King (ISIS)
Biweekly calls
Regular “camps”
Paul Butler (NIST), Stephen King (ISIS) and Nicolas Martinez (ILL) have joined this webinar
Pictures from Code Camps: V, VI, VII, VIII

## Slide 14: Who are we?
SasView ecosystem
Coding
Documentation and tutorials
Computer administration
Project management
Theory
Education and outreach
Physics
Computer Science
Chemistry
Structural Biology
Math/Statistics
Coding is only part of the project!

## Slide 15: Welcome to SasView

## Slide 16: 70+ models to explain 1D data
Data management
Common data formats
Analysis Tool Choice
&
Plotting
Polydispersity (choice of distribution and distribution parameters)
Resolution smearing (pinhole and slit)
Automatically from data or provide parameters
Wide choice of built-in models (> 70)
F(Q), S(Q)
Single, batch and simultaneous fitting
SasView in action

## Slide 17: 2D analysis can be performed fast
Orientational polydispersity = “jitter”
Decouples the frame for the object’s orientation with respect to the beam and the “jitter” around the axis of the object.
Turning on GPU Option highly recommended for 2D fitting

## Slide 18: SasView can analyze SESANS data
SESANS measures structures of materials (20nm-20µm) in real space
Automatic Hankel Transform of SANS models

## Slide 19: Integration with bumps enables multiple fitting engines
Uses bumps package from P. Kienzle
Conventional and Bayesian optimization
Uncertainty estimation of inferred parameters
Parameters correlations

## Slide 20: It is easy to add plugin models
Easy to develop custom models
Syntax and performance testing
Directly available in SasView ecosystem

## Slide 21: And execute them fast...
SasView supports python and c files
Performance optimization (GPU and multi-core)
Full model description
Unit testing

## Slide 22: But what if we don’t know the model
Porod (Scattering) invariant can be applied to multiphase systems
Provide independent estimate of volume fractions (porosity) and surface area (reactivity)
It can be used as sanity check
Notes: For any multi-phase system, i.e. any system that contains regions with different scattering length densities (SLD), the integral over all $vec{q}$ of the appropriately dimensionally-weighted scattering cross-section (ie, 'intensity', $I(vec{q})$ in absolute units) is a constant directly proportional to the mean-square average fluctuation (SLD) and the phase composition. Usefully, this value is independent of the sizes, shapes, or interactions, or, more generally, the arrangement, of the phase domains (i.e. it is invariant) provided the system is incompressible (i.e, the relative volume fractions of the phases do not change). For the purposes of this discussion, a phase is any portion of the material which has a SLD that is distinctly different from the average SLD of the material. This constant is known as the Scattering Invariant, the Porod Invariant, or simply as the Invariant, $Q^*$.

## Slide 23: But what if we don’t know the model
P(r) - probability of finding a vector of length r between scattering centers
In SasView P(r) is derived with Moore’s derivation
Dmax
P(r)
r
r
r
r

## Slide 24: Correlation functions
An imaginary rod moving through the structure of the material
SasView returns both the one-dimensional ( Γ1(x) ) and three-dimensional ( Γ3(x) ) correlation functions

## Slide 25: Other functionality
Analysis
Fitting
Invariant
Pr Inversion
Correlation Function
Tools
Data Operation
SLD calculator
Density/Volume calculator
Slit Size Calculator
Kiessig Thickness Calculator
Q Resolution Estimator
Generic Scattering calculator
Orientation Viewer
Python Shell/Editor
Image Viewer
File Converter

## Slide 26: SasView architecture provides various user interfaces

## Slide 27: SasView can be run from python script
Direct use of samodels and bumps optimizer to fit 1D and 2D data
Scripts can be run of computer cluster
Fitting jobs can be defined from GUI and then detached
Before fit
After fit
https://github.com/SasView/sasview/wiki/DevNotes_DevGuide_GettingStarted

## Slide 28: SasView can be run from Python script
https://github.com/SasView/sasview/wiki/DevNotes_DevGuide_GettingStarted

## Slide 29: How to start using SasView?
sasview.org
https://github.com/SasView

## Slide 30: SasView 5.0.2
New features/improvements
sasview # 1355 SasView 5.0 lacks file conversion option in tool menu
sasview # 1480 Added enumeration of plots in the Windows menu, with raising/setting
sasmodels # 211 Reparameterize existing model.
sasmodels # 390 Re-describe Source intensity in model parameter tables
sasmodels # 382 Doc gen speedup, improved random model generation and minor fixes
Bug Fixes
Fixes sasview # 1455 5.0.1 load project generates a second FitPage1
Fixes sasview # 1499 Ess gui 1355 file converter
Fixes sasview # 1501 Update 5.x documentation for Corfunc
Fixes sasview # 1431 When loading plugin model with a spurious unicode character plugin editor crashes
Fixes sasview # 1138 Check package versions in yaml files and setup.py
etc…
Released in April 2020

## Slide 31: SasView RoadMap
Version 5.1
Complete beta approximation
Complete SasView paper
Begin refactor on constraints/sim fits
Start on use P or S array to do P*S … or I/P?
Starton Oriented 1D cuts fitted
Start Advanced “how to fit my data” tutorial
Start work on General Ornstein Zernike solver
PRISM incorporation
McSAS integrated
Roadmap mid 2020 to mid 2021
Architecture manual complete
Identify “custom workflows”
Custom model editor features added like including compare.py integration
Headless operation for realtime analysis started
sascalc separation started
Start work on time-of-flight resolution function
https://github.com/SasView/documents/tree/master/Roadmap

## Slide 32: Day-to-day issues
https://github.com/SasView/sasview/issues

## Slide 33: What SasView cannot do
Molecular and ab initio models are beyond the scope
http://www.smallangles.net/sassie/SASSIE_HOME.html
https://www.embl-hamburg.de/biosaxs/software.html
SASSIE
ATSAS

## Slide 34: Time-resolved SAXS captures virus capsid assembly
Oliver R., Potrzebowski W., Najibi M., MN Pedersen, L Arleth, N Mahmoudi, I Andre (under review)
Time
?

## Slide 35: Capsid assembly proceeds through two intermediates
Parameter | Value
Weight Sp240 | 0.55±0.03
Weight core shell sphere | 0.45±0.05
Core radius [Å] | 172±10
Shell radius [Å] | 30±4
Oliver R., Potrzebowski W., Najibi M., MN Pedersen, L Arleth, N Mahmoudi, I Andre (under review)
For final state we have mixture of capsids
SasView helped out in the initial analysis

## Slide 36: Education and outreach
Website (www.sasview.org)
Documentation
Written Tutorials
Video Tutorials (YouTube)
Taught courses
  Scattering schools
  University courses
E-learning
Twitter
Slack
Mailing Lists
Marketplace
Camps and other events

## Slide 37: Education and outreach
All the work of ISIS Summer Student Lewis O’Driscoll
Website (www.sasview.org)
Documentation
Written Tutorials
Video Tutorials (YouTube)
Taught courses
  Scattering schools
  University courses
E-learning
Twitter
Slack
Mailing Lists
Marketplace
Camps and other events
http://marketplace.sasview.org/

## Slide 38: Education and outreach
  Bootcamp (from basic use to becoming core developer) https://github.com/SasView/documents/blob/master/Training/SasView_Boot_Camp/syllabus.md
  ”Hackathon” (virtual focussed event)
  Code camp X (most likely at Caltech)
Follow news at:
  www.sasview.org
  Mailing list (users@sasview.org)
  https://twitter.com/SasView
Website (www.sasview.org)
Documentation
Written Tutorials
Video Tutorials (YouTube)
Taught courses
  Scattering schools
  University courses
E-learning
Twitter
Slack
Mailing Lists
Marketplace
Camps and other events
Code camp IX

## Slide 39: Come to work with us!
It is not all about coding!
Things people are saying about SansView/SasView
‘SansView is a very helpful tool, very complete and easy to use’ - Niki
‘I want to thank you for this amazing software. It’s UI and options make the interpretation of spectra easier and faster’ - Philippe
‘I really like the SasView software’ - Martin
‘I have been using SasView as my software of choice for fitting SANS data, and I have been very happy with the software’ - Greg
‘I have found SasView very easy to use and the batch fit function is a wonderful time saving tool. I can finally stop making painful excel macros!’ - Andrew
‘I am a new user of SasView and I think it is a very useful and practical tool’ - Arnaud
‘Within 30 seconds…I am completely converted to SasView!’ - Mike
‘Thank you for creating and maintaining SasView. It is an incredibly helpful tool, and I use it regularly’ - Pasha
‘All the best and thank you again to carry on such a good job on SasView’ - Niki
‘Ooooh NICE PROGRAMME!! Hours of fun!’ - Stuart
‘I love such amazing software so much. It help our researches a lot.’ - Po-Wei

## Slide 40: Thank you for listening

## Slide 41: How do we work?
41
Code is open source and publicly hosted at Github
Released under BSD 3-clause license
Open, Collaborative, Community Development
Bi-weekly developer calls
Code Camps
5 Year Roadmap
Bug and Enhancement Ticket System
Code Hosting, Task and bug tracking, and developer/user wiki
Github
Model Marketplace for users to share their models
marketplace.sasview.org
Automated Builds
build.sasview.org
Model Marketplace
DOI for each release

## Slide 42: Contrast matching
Selective deutaration of system parts

## Slide 43: Contrast matching
ecoR124I
Kennaway CK(1), Taylor JE, Song CF, Potrzebowski W, Nicholson W, ... Roberts GA, Artero JB, Bujnicki JM, Trinick J, Kneale GG, Dryden DT. NAR(2012)